Schäf Systemtechnik GmbH

|  | SST |
| --- | --- |

User Manual

Edition 1

Stand 26. Mar. 2017

für:

Dimex Remote 2.2

|  | Name | Date | Signature |
| --- | --- | --- | --- |
| Author | Schäf | 10. Mar. 2016 |  |
| Review | Mayer | 10. Mar. 2016 |  |

# Content

1	Content	2

2	History	3

3	Application	4

3.1	Application of this Document	4

3.2	Application of the Product	4

3.3	Validity	4

3.4	Distribution	4

3.5	Electronic copy	4

3.6	Archiving	4

1	Manufacturer	7

2	Product Application	7

3	Routine Operation	8

3.1    Manually export images and Use Database	9

3.2	Use Auto-Export	10

3.3	Encrypt / decrypt data	10

3.4	Overwrite	11

3.5	Receiving Port	11

3.6	Import Worklist	12

3.7	Delete images / Worklist option	13

3.8	Burn CDs	14

Appendix: Customer Version of User Manual

# History

| Edition | Date | Author | Modification / reason for Modification |
| --- | --- | --- | --- |
| 1 | 10.03.2016 | Schaef | Initial Version |
| 2 | 26.09.2017 | Prilisch | Update 2.2 |

# Application

## Application of this Document

This document is the user manual for the product concerned.

## Application of the Product

The product is used to import worklist to the local system from an external drive and to export DICOM images to an external drive.

## Validity

The validity of the document is not limited in time. The document will be replaced by a successor as required.

## Distribution

This document will be made available in the folder

Technical Documentation for the product Dimex Remote – User Manual

for everybody concerned.

Further places of use are not planned.

Natalia Prilisch is responsible for the correct distribution of the document.

The document has been distributed according to the a.m. distribution list.

Potential users of copies of old versions of this document have been asked to destroy these and not to use them anymore.

Date				Signature: Natalia Prilisch

## Electronic copy

The electronic copy of this file is located under:

\\192.168.0.120\Other\DOC\entwicklungsprojekte\Dimex Remote\05_Technical Documentation\05-08_User Manual\User_Manual_2_remote.doc

## Archiving

Old versions of this document will be archived in the folder old documents <year> in chronological order.

User Manual

Dimex Remote

Version 2.2

1	Content	2

2	History	3

3	Application	4

3.1	Application of this Document	4

3.2	Application of the Product	4

3.3	Validity	4

3.4	Distribution	4

3.5	Electronic copy	4

3.6	Archiving	4

1	Manufacturer	7

2	Product Application	7

3	Routine Operation	8

3.1    Manually export images and Use Database	9

3.2	Use Auto-Export	10

3.3	Encrypt / decrypt data	11

3.4	Overwrite	12

3.5	Receiving Port	13

3.6	Import Worklist	14

3.7	Delete images / Worklist option	15

3.8	Burn CDs	16

# Manufacturer

Schaef Systemtechnik Medizin UG

Falkenstrasse 22

D 91580 Petersaurach

Phone.: 0 98 72 / 20 02

Fax: 0 98 72 / 28 23

EMail: hms@sstmed.com

# Product Application

The product will be used to import a worklist to the local system from an external drive and to export DICOM images to an external drive.

# Routine Operation

Make sure the external drive is connected and the drive name is configured correctly in the general settings of the program.

After configuring the drive correctly you can see the drive status on the bottom right of the program. This information shows you how many images, appointments and free space are available on the configured external drive.

The green color of the circle shows that the drive is now available. If the name of the drive is not configured correctly, the circle will show red.

## 3.1    Manually export images and Use Database

In order to export all images to the external drive click on the button “Export images”.

The images will be exported to the external drive.

If the option “Use Database” is enabled, a study list of available and exported images will be shown on the “Studies” Tab.

It is then possible to query for a specific study date.

When clicking on the button “Export Images”, all studies with the status “Available” will be exported to the drive.

## Use Auto-Export

In order to automatically export the images as soon as they are received please enable the option “Use Auto-Export” on the export settings of the program.

## Encrypt / decrypt data

To use encryption / decryption please enable the option “Encrypt / Decrypt data” in the general settings of the program.

## Overwrite

By enabling the option “Overwrite” images on the external hard drive will be overwritten by exporting them again.

## Receiving Port

In order to change the receiving port you have to change the value inside the textbox “Receiving Port”. Afterwards click “Ok” and restart the program.

This is the port on which the program is receiving images.

## Import Worklist

In order to import appointments from the external hard drive click on the button “Import Worklist”. You can preview the appointments that are currently on the external drive by selecting the tab “Appointments”.

## Delete images / Worklist option

In order to show the delete images and delete worklist buttons you have to activate the option on the export setting of the program and restart Dimex Remote. Those buttons will delete the images / worklist on the external hard drive.

## Burn CDs

In order to burn images to a CD you have to enable the option “Show “Burn CD” Button”.

After enable restart the program.

At the bottom of the program a button “Burn CD” appears.

By clicking the button “Burn CD” a window appears where you can choose the CD drive.

By clicking „Ok“ all images with the status “Available” will be burned on CD.

# VARIOSTORAGE Configuration

## 4.1 DICOM node configuration

Open VARIOSTORAGE and select “Dicom Configuration” on the top menu.

To add a new node click on the button “New” in the bottom right corner:

A new window will open. Please insert the DICOM node information such as the AET, IP address and port and click on the button “OK”.

## 4.2 Configuring and activating GDT Service

Please switch to the tab “Application Configuration” on the top menu and select “GDTWorklist” -> “01”:

Double click on the filed “Device” and enter the AET of the DIMEX Remote that was configured in the previous step:

Double click on the field “GDT-Path” and input the path where the GDT file is saved. Confirm with “OK”.

Double click on the field “GDT-Suffix” and input the suffix of the file is. Confirm with “OK”.

Double click on the field “Modus” and input the value “2”.Confirm with “OK”.

When the configuration is finished, please start the GDTWorklist service. To do so, select “GDTWorklist” on the list on the right hand side, double click on “Service” and input “1”. Confirm with “OK”.

Please start the Worklist service. To do so, select “Worklist” on the list on the right hand side, double click on “Service” and input “1”. Confirm with “OK”.